## Slide 1: IPv6
CyberQuince​
Notes: Let’s touch upon IPv6 a little bit, shall we…

## Slide 2: LACK OF ADDRESSES
0.0.0.0 – 255.255.255.255
= 232
= 4,294,967,296
128 bits = 232
= 340 trillion trillion trillion
2001:db8:1234::f3a0:22c6:f39c/64
Notes: We mentioned in our previous lesson,
where we learned about NAT, that
there’s not enough IP addresses to
satisfy the needs of the World’s Internet.
And NAT is one of the solutions for that.
However, there’s one more solution, and
that’s an improved Internet Protocol.
The IP addressing system we described
earlier is called the “IP version 4”,
and the newer, improved one, is “IP
version 6”.
First, an important statistic.
We calculated that with IPv4, we used
32 bits and that gives us
a little over 4 Billion unique IPs.
With IPv6, we use 1) 128 bits, which is
2 to the power of 128, which iiiiiis…
2) this number.. That’s a lot, right?
Okay, so this is what an IPv6 address
looks like 3)
Let’s take it apart -> to better understand it

## Slide 3
2001:db8:1234::f3a0:22c6:f39c/64
Notes: First off, it’s obviously written in a
different format than IPv4s, in
hexadecimal, and if this looked
a bit long and chaotic, let me
disappoint you some more:
this is a shortened version of
an IPv6 address. And that’s what
we’ll dissect now.
So first, there’s EIGHT of these…
groups, and each group consists
of 16 bits. The groups are, as you
can see here, separated by colons,
So if there are EIGHT groups, we should
be able to count that many, right?
Actually, no. BECAUSE IPv6 addresses
are so long, there are some rules you
can follow to correctly “compress” it.

## Slide 4
2001:db8:1234::f3a0:22c6:f39c/64
0000:0000
If an IPv6 address contains one or more consecutive groups of zeros, they can be replaced by a double colon (::)
“
”
2001:1000:130f:0000:0000:0000:876a:130b
2001:1000:130f::876a:130b
Notes: Let’s count the groups we can see
here: 1), 2), 3), 4), 5), and 6).
And the missing two, are here 7)
Hidden, or, redacted, because
when you see two consecutive
colons in an IPv6 address, that means
that originally, there was just zeroes
8) there.
So let’s define a rule here: 9)
If an IPv6 address contains one
or more consecutive groups of zeros,
they can be replaced by a double colon (::)
Here’s one more example: 10)
this is the full address, and this
would be the shorter format: 11)
However, there’s more opportunities
to redact, so let’s look at that.

## Slide 5
2001:db8:1234::f3a0:22c6:f39c/64
Omit leading zeros in any group of 4 hexadecimal digits: the rule applies only to leading zeros and no trailing zeros. Even if a group consists of 4 zeros we can only omit the leading 3 - 0000.
“
”
Notes: Using our first example, let’s look
at one of the groups in more
detail -> 1) this one, the second group.
We said that there’s 8 groups and each
group holds 16 bits. One hexadecimal
character if 4 bits, therefore, there should
be 4 characters in each group.
But in THIS group, there’s only three. Where
did the fourth go?
Actually, it’s not the fourth that’s missing,
but the first 2).
And THAT is another rule for us to write 3)
down: “Omit leading zeros in any group
of 4 hexadecimal digits: the rule applies
only to leading zeros and no trailing
zeros. Even if a group consists of 4
zeros we can only omit the leading 3.”

## Slide 6
2001:0df8:00f2:0000:0000:0000:0000:0f11
2001:df8:f2::f11
2001
0df8
00f2
0f11
Notes: Let’s look at another example.
We have here the full IP address.
and I’ve just now highlighted all
the zeros that CAN be redacted.
The two zeros 2) in the first group can’t
be shortened. That’s just the rule.
All right, let’s see what the address
looks 3) shortened. Here it is.
Let’s imagine you as a network
engineer see this somewhere and need
to understand what was the full address.
We’ll start from the first group 4) – there’s
four characters, so 5) that one’s complete.
Next one, 6) has only three characters –
that means that ONE leading zero has
been omitted 7). Next, 8) there’s TWO
characters in the group – that means
TWO zeros are missing 9). And
eventually we reach this double colon
here 10) but in order to know just
HOW MANY zeroes were omitted,
we need to look at the rest of the
address, and our final group 11)
is three characters, which means
only one zero is missing 12).
And back to the double colons,

## Slide 7
2001:0df8:00f2:0000:0000:0000:0000:0f11
2001:df8:f2::f11
0000:0000:0000:0000
Notes: we counted 1) 4 groups that we analyzed
and reversed back to the full format. So
with 4 we CAN see, it means that another
four are missing. Because in total there’s
eight groups in total in every IPv6 address.
THAT brings us to the conclusion that 2)
this is what’s hidden behind those two
colons, because, as we already defined,
only consecutive zeros can be omitted
like this.
NOW, you might wonder – what if there’s
consecutive zeros in multiple places
in the address?

## Slide 8
2001:8cbe:0000:0000:1fc2:0000:0000:f0b9
2001:8cbe::1fc2:0:0:f0b9
Replacement of consecutive zeros can only be applied once, because otherwise, the original IPv6 address cannot be recreated from the shortened representation.
“
”
2001:8cbe:0:0:1fc2::f0b9
2001:8cbe::1fc2::f0b9
Notes: Let’s take this IP as an example.
We have consecutive zeros in
two 1) places here. And this is
a perfect time to introduce another,
and final – don’t worry  - rule
for shortening IPv6 addresses,
2) Replacement of consecutive
zeros can only be applied once,
because otherwise, the original IPv6
address cannot be recreated from
the shortened representation.
In other words, we can only do
this 3), OR this 4) – both are valid by
the way.
THIS 5) is not allowed – replacing both
groups of zeros with double colons.
All right,

## Slide 9: IPV6
CyberQuince
Notes: Other than that, the subnet mask,
allocating addresses et cetera is pretty
similar to IPv4, so we’re going to stop
right here.
See you in the next lesson 